## Slide 1
CODEALPHA • INTERNET OF THINGS
AUTOMATIC LIGHT
CONTROL USING LDR
Task 2 — Sensor-Based Simulation
Student: Niharika Varshitha T.
Platform: Tinkercad Circuits • Board: Arduino Uno R3
SIMULATED PROJECT PRESENTATION

## Slide 2
1. Objective
CodeAlpha IoT Internship • Task 2 02
To design and simulate an automatic light control system using an LDR sensor and Arduino Uno. The system detects light intensity and controls an LED according to the sensor reading.
SENSE
LDR detects light
PROCESS
Arduino checks value
RESPOND
LED turns ON or OFF

## Slide 3
2. Components Used
CodeAlpha IoT Internship • Task 2 03
Arduino Uno R3
Reads the sensor and controls the LED
LDR / Photoresistor
Senses surrounding light
LED
Shows the system output
1 kΩ resistor
Limits current through the LED
10 kΩ resistor
Forms a voltage divider with LDR
Breadboard & jumper wires
Connect the components
Tinkercad Circuits
Online simulation environment

## Slide 4
3. Circuit Connections
CodeAlpha IoT Internship • Task 2 04
INSERT Task2_Circuit.png
Replace this box with your saved screenshot
• LDR output junction → A0
• LED control pin → D9
• 1 kΩ resistor in series with LED
• 10 kΩ resistor from LDR junction to GND
• LDR connected to 5V
• Common ground (GND)

## Slide 5
4. Working Principle
CodeAlpha IoT Internship • Task 2 05
1
LDR senses light
Sensor produces an analog reading.
2
Arduino reads A0
The value is checked repeatedly.
3
Compare with 500
The program uses 500 as its threshold.
4
Control the LED
Below 500: ON • 500 or above: OFF.

## Slide 6
5. Arduino Program
CodeAlpha IoT Internship • Task 2 06
const int ldrPin = A0;
const int ledPin = 9;
const int threshold = 500;
void setup() {
pinMode(ledPin, OUTPUT);
Serial.begin(9600);
}
void loop() {
int lightLevel = analogRead(ldrPin);
if (lightLevel < threshold) {
digitalWrite(ledPin, HIGH);
} else {
digitalWrite(ledPin, LOW);
}
Serial.println(lightLevel);
delay(200);
}
INSERT Task2_Code.png
Replace this box with your saved screenshot
Threshold = 500
LED pin = 9 • LDR pin = A0

## Slide 7
6. Code Explanation
CodeAlpha IoT Internship • Task 2 07
A0
Analog input used to read the LDR value.
Pin 9
Digital output used to control the LED.
Threshold 500
Reference value for switching the LED.
analogRead()
Reads the current sensor value.
digitalWrite()
Sets the LED output HIGH or LOW.
Serial.println()
Displays readings in the Serial Monitor.
delay(200)
Waits 200 milliseconds between readings.

## Slide 8
7. Simulation Result — LED ON
CodeAlpha IoT Internship • Task 2 08
INSERT Task2_LED_ON.png
Replace this box with your saved screenshot
LOW-LIGHT TEST
Example reading
54 (below 500)
LED STATUS: ON
The LED glows when the reading is below 500.

## Slide 9
8. Simulation Result — LED OFF
CodeAlpha IoT Internship • Task 2 09
INSERT Task2_LED_OFF.png
Replace this box with your saved screenshot
HIGH-READING TEST
Example reading
973 (above 500)
LED STATUS: OFF
The LED switches off when the reading is above 500.

## Slide 10
9. Overall Result
CodeAlpha IoT Internship • Task 2 10
The circuit responded to sensor readings and switched the LED according to the programmed threshold.
LDR reading < 500
Low-light test
LED ON
LDR reading = 500
At threshold
LED OFF
LDR reading > 500
High-reading test
LED OFF
Note: A reading equal to 500 follows the ELSE branch, so the LED is OFF.

## Slide 11
CONCLUSION
The project demonstrates a simple sensor-based automation system. The LDR provides an input reading, and the Arduino processes it to control an LED automatically.
THANK YOU
CodeAlpha IoT Internship • Task 2